## Slide 1
Battery
Battery
Master Switch
Wheel Driver
Wheel Driver
Wheel Driver
Wheel Driver
Wheel Driver
Wheel Driver
Master Control Board
Arm Control Board
Drive Control Board
Power Relay
Power Relay
Power Relay
Arm
Power Relays should Have a local override
Legend:
Power
Signal
Module
Communications
(radios)
Notes: Electrical architecture. Shows power systems, components, and communication lines.

## Slide 2
Master Control Board
Arm Control Board
Drive Control Board
Comms. Interface
Comms. Interface
Comms. Interface
External Debug
(Sees everything, renders whatever we need to the user)
(May comprise of rqt tools)
Wheel Control
Left
Right
Speed Control
Left
Right
Speed
Turn
Base Station Interface
GPS
Status Indicators & Debug GPIOs
Linear Actuator Driver
Servo Driver
(smoothing etc.
included)
Inverse Kinematics
Soil Science System
Notes: ROS Architecture. Structure of nodes (lines are topics).
The Comms. Interface nodes will handle communication between the boards. They are intended as the only interface between boards. To be clear: the master control board should not publish or subscribe to internal topics of the other boards.
The base station may communicate over ROS, but that will depend on the network reliability, and on if we are using a TCP/IP enabled communications system.
The Inverse Kinematics library may or may not exist in reality. It will certainty not exist in rev1.